## Slide 1
ENGINEERING MINI PROJECT
SMART
DUSTBIN
Touchless waste disposal using Arduino and an ultrasonic sensor
AUTOMATION • HYGIENE
HC-SR04
Arduino Uno + Servo
GROUP MEMBERS
1. Shaur Shaikh
2. Suyash Hatankar
3. Kanishk Patil
4. Siddhi Aghav

## Slide 2
PROJECT OVERVIEW
02 / 14
What is a Smart Dustbin?
A simple automated bin that opens without the user touching the lid.
SMART DUSTBIN • MINI PROJECT
TOUCHLESS
The lid opens when a hand or object comes near the sensor.
AUTOMATIC
Arduino processes the sensor reading and controls the servo motor.
HYGIENIC
Reduces direct contact with the bin lid and supports cleaner disposal.

## Slide 3
NEED FOR THE PROJECT
03 / 14
Problem Statement
Traditional bins often require users to touch the lid or pedal.
SMART DUSTBIN • MINI PROJECT
Hygiene concerns
Touching a shared bin lid can spread dirt and germs.
Everyday inconvenience
Opening a bin can be difficult when hands are full.
Poor waste habits
A convenient bin can encourage people to dispose of waste properly.
Need for automation
Low-cost sensors and microcontrollers can automate simple tasks.

## Slide 4
PROJECT GOALS
04 / 14
Objectives
What this project aims to achieve.
SMART DUSTBIN • MINI PROJECT
01
Detect nearby objects
Use the HC-SR04 ultrasonic sensor.
02
Open the lid automatically
Move the lid using a servo motor.
03
Close after a short delay
Return the lid to its closed position.
04
Build at low cost
Use simple, commonly available components.

## Slide 5
HARDWARE
05 / 14
Components Required
The main parts used to build the prototype.
SMART DUSTBIN • MINI PROJECT
Arduino Uno
The controller that reads sensor data and commands the servo.
HC-SR04 ultrasonic sensor
Measures distance to a hand or object in front of the bin.
Servo motor
Moves the lid open and closed.
9V battery + connector
Provides power for the prototype; check suitable power regulation.
Jumper wires
Connect the sensor, servo and controller.
Bin with hinged lid
The physical container for waste.

## Slide 6
SYSTEM DESIGN
06 / 14
Block Diagram
Signal flow from object detection to lid movement.
SMART DUSTBIN • MINI PROJECT
Hand / Object
Near the bin
HC-SR04
Distance reading
Arduino Uno
Decision logic
Servo Motor
Lid movement
Dustbin Lid
Open / close
→
→
→
→
Power supply: 9V battery + connector (use suitable regulated supply for the board and servo).

## Slide 7
HOW IT SENSES
07 / 14
HC-SR04 Ultrasonic Sensor
It estimates distance using the time taken by an ultrasonic echo.
SMART DUSTBIN • MINI PROJECT
TRIG
Arduino sends a short trigger pulse; the sensor emits ultrasonic sound waves.
ECHO
The returning echo pulse duration is used to estimate the distance.
Distance ≈ (Echo time × speed of sound) ÷ 2

## Slide 8
MOTION CONTROL
08 / 14
Role of the Servo Motor
The servo turns to a chosen angle to lift and lower the lid.
SMART DUSTBIN • MINI PROJECT
CLOSED POSITION
The lid rests over the bin when no object is detected.
OPEN POSITION
The servo rotates to lift the lid when the sensor detects a nearby object.
RETURN
After a short delay, the servo returns the lid to its closed position.
A lightweight lid and a secure servo linkage help the mechanism work reliably.

## Slide 9
OPERATION
09 / 14
Working Principle
A simple four-step automatic cycle.
SMART DUSTBIN • MINI PROJECT
01
Detect
The HC-SR04 measures the distance to a hand or object.
02
Decide
Arduino compares the distance with a set threshold.
03
Open
Arduino commands the servo to open the lid.
04
Close
After a brief wait, the servo closes the lid.

## Slide 10
CONTROL LOGIC
10 / 14
Algorithm / Flowchart
The program repeats this sequence continuously.
SMART DUSTBIN • MINI PROJECT
START
Read distance
Object within range?
YES → Open lid
NO → Keep closed
YES
NO
Wait briefly → close lid → repeat from distance reading
Illustrative logic; the Arduino sketch defines the exact threshold, angle and delay.

## Slide 11
ADVANTAGES
11 / 14
Project Benefits
Practical benefits of a touchless waste bin.
SMART DUSTBIN • MINI PROJECT
More hygienic
Less need to touch the lid.
Convenient
Can be used when hands are occupied.
Automatic
Opens and closes with minimal user effort.
Affordable prototype
Uses widely available electronic components.
Educational
Demonstrates sensors, control and embedded programming.
Expandable
Can later add a full-bin sensor or buzzer.

## Slide 12
USE CASES
12 / 14
Applications
Where a smart dustbin can be useful.
SMART DUSTBIN • MINI PROJECT
Homes
Kitchen and common areas
Schools & colleges
Classrooms, labs and corridors
Offices
Shared workspaces and meeting areas
Clinics
Areas where touchless disposal is useful

## Slide 13
IMPROVEMENTS
13 / 14
Limitations & Future Scope
Possible upgrades for a more reliable smart waste system.
SMART DUSTBIN • MINI PROJECT
CURRENT LIMITATIONS
• Limited detection range
• Battery needs recharging/replacement
• Lid mechanism needs careful alignment
FUTURE ENHANCEMENTS
• Full-bin sensor and buzzer
• Wi-Fi / IoT notifications
• Solar or rechargeable power
• Improved enclosure and lid linkage
Note: Fill-level monitoring and phone alerts are optional and are not part of the basic component list.

## Slide 14
CONCLUSION
A small step toward
smarter, cleaner disposal.
SMART DUSTBIN uses an ultrasonic sensor, Arduino Uno and servo motor to automate lid movement. The prototype demonstrates how embedded systems can make everyday tasks more convenient and hygienic.
THANK YOU
Questions?
SMART DUSTBIN • MINI PROJECT